Copyright 2018 by The American Institute of Architects (AIA)

Exclusively published and distributed by Deltek Inc for the AIA

This Product MasterSpec Section is licensed by Deltek Inc. to Jay R. Smith Manufacturing ("Licensee").

This Product MasterSpec Section modifies the original MasterSpec text and does not include the full content of the original MasterSpec Section.

Revisions made to the original MasterSpec text are made solely by the Licensee and are not endorsed by, or representative of the opinions of, Deltek or The American Institute of Architects (AIA). Neither AIA nor Deltek are liable in any way for such revisions or for the use of this Product MasterSpec Section by any end user. A qualified design professional should review and edit the document to suit project requirements.

For more information, contact Jay R. Smith Manufacturing, 2781 Gunter Park Dr. E, Montgomery, AL 36109; Phone: (334) 272-7396 | (800) 467-6484; Fax: Fax: (334) 272-7396; Website: www.jrsmith.com; Email: salesengineering@jrsmith.com.

For information about MasterSpec, contact Deltek at (800) 424-5080 or visit Masterspec.com.

SECTION 221319.13 - SANITARY DRAINS

TIPS:

To view non-printing Editor's Notes that provide guidance for editing, click on MasterWorks/Single-File Formatting/Toggle/Editor's Notes.

To read detailed research, technical information about products and materials, and coordination checklists, click on MasterWorks/Supporting Information.

Access Product MasterSpec Sections:

<Double click here to view the list of manufacturer Sections available at ProductMasterSpec.com.>

Revise this Section by deleting and inserting text to meet Project-specific requirements.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

SUMMARY

Section Includes:

Floor drains.

Floor sinks.

Trench drains.

Channel drainage systems.

DEFINITIONS

Retain terms that remain after this Section has been edited for a project.

ABS: Acrylonitrile-butadiene styrene.

FRP: Fiberglass-reinforced plastic.

HDPE: High-density polyethylene.

PE: Polyethylene.

PP: Polypropylene.

PVC: Polyvinyl chloride.

ACTION SUBMITTALS

Product Data: For each type of product.

PRODUCTS

Manufacturers and products listed in this Section are neither recommended nor endorsed by the AIA or Deltek. Before selecting manufacturers and products, verify availability, suitability for intended applications, and compliance with minimum performance requirements. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

Product options commonly available from manufacturers are included in square brackets throughout the Section Text. Not every manufacturer listed can provide every option offered; verify availability with manufacturers. For definitions of terms and requirements for Contractor's product selection, see Section 016000 "Product Requirements."

DRAIN ASSEMBLIES

Sanitary drains shall bear label, stamp, or other markings of specified testing agency.

Comply with NSF 14 for plastic sanitary piping specialty components.

FLOOR DRAINS

Copy paragraphs below and re-edit for each product.

Insert drawing designation for each product required. Use these designations on Drawings to identify each product.

Cast-Iron Floor Drains <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 2005-A option for round-top or model 2005-B for square-top floor or shower drains.

Retain model 2005-69 option for round shower drains with adjustable height and heavy-duty grating.

Retain model 2005-TT option for round floor or shower drains with tilt-top and adjustable height.

Retain model 2015 option for round or square floor or shower drains with adjustable height.

Retain model 2120 option for heavy-duty 8.5-inch round drains with tractor grate.

Retain model 2141 option for heavy duty 12-inch round drains with tractor grate.

Retain model 2320 option for medium duty 8.5-inch round drains with tractor grate and adjustable height.

Retain model 2500 option for flushing-type laboratory and institutional floor drains.

Retain model 2505 option for flushing-type laboratory and institutional floor drains with integral trap.

Retain model 2624 for parking deck drains.

          - Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing model [2005-A] [2005-B] [2005-69] [2005-TT] [2015] [2120] [2141] [2320] [2500] [2505] [2624]; <Insert product name or designation> or comparable product by one of the following:

Commercial Enameling Company.

Josam Company.

MIFAB, Inc.

Prier Products, Inc.

Sioux Chief Manufacturing Company, Inc.

Wade; a subsidiary of McWane Inc.

WATTS.

Zurn Industries, LLC.

<Insert manufacturer's name>.

Standard: ASME A112.6.3[ with backwater valve].

Pattern: [Area] [Floor] [Funnel floor] [Sanitary] <Insert pattern> drain.

Body Material: [Gray iron] <Insert material>.

Accessories:

Retain any of 17 subparagraphs below to conform to Project design.

Seepage Flange.

Anchor Flange.

Clamping Device.

Outlet: [Bottom] [Side] <Insert Outlet type>.

Backwater Valve: Drain-outlet, [ASME A112.14.1, integral], [swing-check] type.

Retain coating in "Coating on Interior and Exposed Exterior Surfaces" Subparagraph below when required for sanitary floor drains.

Coating on Interior and Exposed Exterior Surfaces: [Acid-resistant enamel] <Insert material>.

Sediment Bucket.

Top or Strainer Material: [Bronze] [Gray iron] [Nickel bronze] [Stainless steel] <Insert material>.

Top of Body and Strainer Finish: [Nickel bronze] [Polished bronze] [Rough bronze] [Stainless steel] <Insert finish>.

Top Shape: [Round] [Square] <Insert shape>.

Dimensions of Top or Strainer: <Insert dimensions and describe body, sump, and grate>.

Top Loading Classification: [Extra Heavy] [Heavy] [Light] [Medium] duty.

Funnel: <Insert description and dimensions>.

Inlet Fitting: Gray iron, with threaded inlet and threaded or spigot outlet, and trap-seal primer valve connection.

Trap Material: [Bronze] [Cast iron] [Copper] <Insert material>.

Trap Pattern: [Deep-seal P-trap] [Standard P-trap] <Insert pattern>.

Trap Features: [Cleanout] [Trap-seal primer valve drain connection] [Cleanout and trap-seal primer valve drain connection] <Insert type>.

Stainless Steel Floor Drains, ASME A112.3.1 <Insert drawing designation if any>:

Retain "Manufacturers" Subparagraph and list of manufacturers below to require products from manufacturers listed or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by the following:

Zurn Industries, LLC.

<Insert manufacturer's name>.

Outlet: [Bottom] [Side] <Insert type>.

Top or Strainer Material: [Stainless steel] <Insert material>.

Top Shape: [Round] [Square] <Insert shape>.

Dimensions of Top or Strainer: <Insert dimensions and describe body, sump, and grate>.

Seepage Flange: [Not required] [Required].

Anchor Flange: [Not required] [Required].

Clamping Device: [Not required] [Required].

Trap-Primer Connection: [Not required] [Required].

Trap Material: [Cast iron] [Stainless steel] [Not required] <Insert material>.

Trap Pattern: [Deep-seal P-trap] [Standard P-trap] [Not required] <Insert pattern>.

Stainless Steel Floor Drains, ASME A112.6.3 <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 9620 option for 10-inch round floor drains.

Retain model 9630 option for 12-inch round floor drains.

Retain model 9700 option for 7-inch round stainless or carbon steel drains with adjustable height.

Retain model 9705 option for 8.5-inch round, medium duty, stainless or carbon steel drains with adjustable height.

Retain model 9710 option for 8.5-inch round, medium duty, stainless or carbon steel drains.

Retain model 9725 option for 8.5-inch round, medium duty, stainless or carbon steel drains with adjustable height.

Retain model 9730 option for 12-inch round, heavy duty, stainless or carbon steel drains.

Retain model 9733 option for 15-inch round, heavy duty, stainless or carbon steel drains.

Retain model 9750 option for 8-inch round, medium duty, stainless or carbon steel drains with integral trap and floor level cleanout.

          - Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; model [9620] [9630] [9700] [9705] [9710] [9725] [9730] [9733] [9750]; <Insert product name or designation> or comparable product by one of the following:

Josam Company.

Kusel Equipment Co.

Scherping Systems, Inc.

Sioux Chief Manufacturing Company, Inc.

Wade; a subsidiary of McWane Inc.

WATTS.

Zurn Industries, LLC.

<Insert manufacturer's name>.

Outlet: [Bottom] [Side] <Insert type>.

Top or Strainer Material: [Stainless steel] <Insert material>.

Top Shape: [Round] [Square] <Insert shape>.

Dimensions of Top or Strainer: <Insert dimensions and describe body, sump, and grate>.

Accessories:

Retain any of seven subparagraphs below to conform to Project design.

Seepage Flange.

Anchor Flange.

Clamping Device.

Trap-Primer Connection.

Trap Material: [Cast iron] [Stainless steel] <Insert material>.

Trap Pattern: [Deep-seal P-trap] [Standard P-trap] <Insert pattern>.

<Insert additional accessories>.

Plastic Floor Drains <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 202 option for 4.75-inch round PVC floor drains.

Retain model 215 option for 4.25-inch round ABS floor drains.

Retain model 216 option for 4.25-inch round PVC floor drains.

Retain model 225 option for 8.5-inch round PVC floor drains.

          - Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; model [202] [215] [216] [225]; <Insert product name or designation> or comparable product by one of the following:

Canplas LLC.

IPS Corporation.

Josam Company.

Oatey.

Plastic Oddities.

Sioux Chief Manufacturing Company, Inc.

Zurn Industries, LLC.

<Insert manufacturer's name>.

Standard: ASME A112.6.3.

Material: [ABS] [or] [PVC] <Insert material>.

Accessories:

Retain any of 11 subparagraphs below to conform to the project design.

Seepage Flange.

Clamping Device.

Outlet: [Bottom] [Side] <Insert type>.

Sediment Bucket.

Top or Strainer Material: Plastic.

Top of Body and Strainer Finish: Plastic.

Top Shape: Round.

Dimensions of Top or Strainer: <Insert dimensions and describe body, sump, and grate if required>.

Trap Material: Plastic drainage piping.

Trap Pattern: [Standard P-trap] <Insert pattern>.

<Insert additional accessories>.

FLOOR SINKS

Copy paragraphs below and re-edit for each product.

Insert drawing designation for each product required. Use these designations on Drawings to identify each product.

Cast-Iron Floor Sinks <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 3020 option for 8.5-inch round acid-resistant coated floor and indirect drains.

Retain model 3030 option for 12.5-inch round acid-resistant coated floor and indirect drains.

Retain model 3040 option for 8.5-inch round acid-resistant coated floor and indirect drains.

Retain model 3060 option for 12.5-inch round acid-resistant coated floor and indirect drains with deep receptors.

Retain model 3100 option for 8.5-inch square acid-resistant coated floor and indirect drains.

Retain model 3140 option for 12.5-inch square acid-resistant coated floor and indirect drains with deep receptors.

Retain model 3200 option for 16.5-inch square acid-resistant coated floor and indirect drains with deep receptors.

Retain model 3400 option for 12-inch-diameter acid-resistant coated floor and indirect drains with deep receptors and non-traffic tops.

Retain model 3410 option for 8-inch square acid-resistant coated floor and indirect drains with deep receptors and non-traffic tops.

Retain model 3420 option for 12-inch square acid-resistant coated floor and indirect drains with deep receptors and non-traffic tops.

Retain model 3450 option for 16-inch square acid-resistant coated floor and indirect drains with deep receptors and non-traffic tops.

          - Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; model [3020] [3030] [3040] [3060] [3100] [3140] [3200] [3400] [3410] [3420] [3450]; <Insert product name or designation> or comparable product by one of the following:

Commercial Enameling Company.

Josam Company.

Wade; a subsidiary of McWane Inc.

Watts; a Watts Water Technologies company.

Zurn Industries, LLC.

<Insert manufacturer's name>.

Standard: ASME A112.6.7.

Pattern: [Floor] [Funnel floor] <Insert pattern> drain.

Body Material: Cast iron.

Accessories:

Retain any of 14 subparagraphs below to conform to Project design.

Anchor Flange: [With] [Without] seepage holes.

Clamping Device.

Outlet: Bottom, [no-hub] <Insert type> connection.

Coating on Interior Surfaces: [Acid-resistant enamel] <Insert coating>.

Sediment Bucket.

Internal Strainer: [Dome] [Flat].

Internal Strainer Material: [Aluminum] <Insert material>.

Top Grate Material: [Cast iron] <Insert material> [, loose] [, hinged].

Top of Body and Grate Finish: [Nickel bronze] [Acid-resistant enamel] <Insert finish>.

Top Shape: [Round] [Square] <Insert shape>.

Dimensions of Top Grate: <Insert dimensions and describe grate pattern>.

Top Loading Classification: [No traffic] <Insert traffic loading>.

Funnel: <Insert material, shape, and dimensions>.

<Insert additional accessories>.

Stainless Steel Floor Sinks, ASME A112.6.7 <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 3001 option for 12-inch square stainless steel floor and indirect drains with deep receptors.

Retain model DX3001 option for 17.5-inch square stainless steel floor and indirect drains with deep receptors.

Retain model 9691 option for 12-inch square 14 GA stainless steel floor and indirect drains with deep receptors.

          - Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; model [3001] [DX3001] [9691]; <Insert product name or designation> or comparable product by one of the following:

Josam Company.

Wade; a subsidiary of McWane Inc.

Watts; a Watts Water Technologies company.

Zurn Industries, LLC.

<Insert manufacturer's name>.

Standard: ASME A112.6.7.

Pattern: [Floor] [Funnel floor] <Insert pattern> drain.

Body Material: Stainless steel.

Accessories:

Retain any of 13 subparagraphs below to conform to Project design.

Anchor Flange: [With] [Without] seepage holes.

Clamping Device.

Outlet: Bottom, [no-hub] <Insert type> connection.

Sediment Bucket.

Internal Strainer: [Dome] [Flat].

Internal Strainer Material: [Stainless steel] <Insert material>.

Top Grate Material: [Stainless steel] <Insert material> [, loose] [, hinged].

Top of Body and Grate Finish: [Satin nickel] [Stainless steel] <Insert finish>.

Top Shape: [Round] [Square] <Insert shape>.

Dimensions of Top Grate: <Insert dimensions and describe grate pattern>.

Top Loading Classification: [No traffic] <Insert traffic loading>.

Funnel: <Insert material, shape, and dimensions>.

<Insert additional accessories>.

Plastic Floor Sinks <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 3142 option for PVC floor sink with dome bottom strainer.

Retain model 3143 option for PVC floor sink with sediment bucket.

Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; model [3142] [3143]; <Insert product name or designation>

Canplas LLC.

IPS Corporation.

Oatey.

Plastic Oddities.

Sioux Chief Manufacturing Company, Inc.

<Insert manufacturer's name>.

Standard: ASME A112.6.7.

Pattern: [Floor] [Funnel floor] <Insert pattern> drain.

Body Material: PVC.

Outlet: Bottom, PVC primer and solvent cement connection.

Retain one or more of nine subparagraphs below when required by project design.

Sediment Bucket: <Insert description>.

Internal Strainer: [Dome] [Flat].

Internal Strainer Material: [PVC] <Insert material>.

Top Grate Material: [PVC] <Insert material>.

Top Shape: [Round] [Square] <Insert shape>.

Dimensions of Top Grate: <Insert dimensions and describe grate pattern>.

Top Loading Classification: [No traffic] <Insert traffic loading>.

Funnel: <Insert material, shape and dimensions>.

<Insert additional accessories>.

TRENCH DRAINS

Copy paragraph below and re-edit for each product.

Insert drawing designation for each product required. Use these designations on Drawings to identify each product.

Trench Drains <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 2710 option for 12-inch-wide drains.

Retain model 2810 option for 6-inch-wide drains.

          - Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; [2710] [2810]; <Insert product name or designation> or comparable product by one of the following:

Josam Company.

MIFAB, Inc.

Sioux Chief Manufacturing Company, Inc.

Wade; a subsidiary of McWane Inc.

WATTS.

Zurn Industries, LLC.

<Insert manufacturer's name>.

Standard: ASME A112.6.3 for trench drains.

Material: Ductile or gray iron.

Accessories:

Retain any of 10 subparagraphs below to conform to Project design.

Flange: [Anchor] [Seepage].

Clamping Device.

Outlet: [Bottom] [End] [Side] <Insert location>.

Grate Material: [Ductile iron] [Ductile iron or gray iron] [Gray iron] [Stainless steel] <Insert material>.

Grate Finish: [Painted] <Insert finish>.

Dimensions of Frame and Grate: <Insert dimensions and describe body, sump, and grate if required>.

Top Loading Classification: [Extra Heavy Duty] [Heavy Duty] [Light Duty] [Medium Duty] <Delete if not applicable>.

Trap Material: [Cast iron] [Stainless steel] <Insert material>.

Trap Pattern: [Standard P-trap] <Insert pattern>.

<Insert additional accessories>.

CHANNEL DRAINAGE SYSTEMS

Copy paragraphs below and re-edit for each product.

Insert drawing designation for each product required. Use these designations on Drawings to identify each product.

Retain first paragraph and related subparagraphs below for channel drains required to comply with ASME A112.3.1.

Stainless Steel Channel Drainage Systems, ASME A112.3.1 <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 9660 option for 6-inch-wide stainless steel trench drains.

Retain model 9666 option for 2-inch-wide stainless steel sloped trench drains.

Retain model 9667 option for 2-inch-wide stainless steel non-sloped trench drains.

Retain model 9670 option for 14-inch-wide modular stainless steel trench drains.

Retain model 9671 option for modular stainless steel trench drains with 0.75-inch slots.

Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; [9660] [9666] [9667] [9670] [9671]; <Insert product name or designation> or comparable product by one of the following:

Josam Company.

<Insert manufacturer's name>.

Description: Modular system of stainless steel channel sections, grates, and appurtenances; designed so grates fit into channel recesses without rocking or rattling.

Standard: ASME A112.3.1 for trench drains.

Channel Sections: Interlocking joint, stainless steel with level invert.

Dimensions: [2.0 inches (51 mm)] [6.0 inches (152 mm)] [14 inches (356 mm)] wide. Include number of units required to form total lengths indicated.

Grates: Manufacturer's designation "[heavy] [medium] duty," with slots or perforations, and of width and thickness that fit recesses in channels.

Material: [Stainless steel] <Insert material>.

Locking Mechanism: [Manufacturer's standard device for securing grates to channel sections].

Indicate locations and lengths of covers on Drawings.

Covers: Solid [stainless steel] <Insert material>, of width and thickness that fit recesses in channels, and of lengths indicated.

Supports, Anchors, and Setting Devices: Manufacturer's standard, unless otherwise indicated.

Channel-Section Joining and Fastening Materials: As recommended by system manufacturer.

Retain first paragraph and related subparagraphs below for channel drains not required to comply with ASME A112.3.1.

Stainless Steel Channel Drainage Systems, Non-ASME A112.3.1 <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; model 9660; <Insert product name or designation> or comparable product by one of the following:

MultiDrain Systems, Inc.

Zurn Industries, LLC.

<Insert manufacturer's name>.

Description: Modular system of stainless steel channel sections, grates, and appurtenances; designed so grates fit into channel recesses without rocking or rattling.

Channel Sections: Interlocking joint, stainless steel with level invert.

Dimensions: [6 inches (152 mm)] [12 inches (305 mm)] wide. Include number of units required to form total lengths indicated.

Grates: Manufacturer's designation "[heavy] [medium] duty," with slots or perforations, and of width and thickness that fit recesses in channels.

Material: [Ductile iron] [Fiberglass] [Galvanized steel] [Gray iron] [Stainless steel] <Insert material>.

Locking Mechanism: [Manufacturer's standard device for securing grates to channel sections] [Not required].

Indicate locations and lengths of covers on Drawings.

Covers: Solid [ductile or gray iron] [stainless steel] <Insert material>, of width and thickness that fit recesses in channels, and of lengths indicated.

Supports, Anchors, and Setting Devices: Manufacturer's standard, unless otherwise indicated.

Channel-Section Joining and Fastening Materials: As recommended by system manufacturer.

Narrow, Sloped-Invert, Polymer-Concrete Channel Drainage Systems <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 9877 option for 6-inch-wide polymer concrete trench drain.

Retain model 9895 option for 6-inch-wide polymer concrete trench drain with integral metal rail.

          - Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; [9877] [9895]; <Insert product name or designation> or comparable product by one of the following:

ABT, Inc.

ACO USA.

Forté Composites, Inc.

Josam Company.

Polycast: Hubbell Power Systems, Inc.

<Insert manufacturer's name>.

Description: Modular system of channel sections, grates, and appurtenances; designed so grates fit into channel recesses without rocking or rattling.

Channel Sections: Narrow, interlocking-joint, sloped-invert, polymer-concrete modular units with end caps.

Include rounded bottom, with built-in invert slope of 0.6 percent and with outlets in number, sizes, and locations indicated.

Include extension sections necessary for required depth.

Dimensions: 4-inch (102-mm) inside width. Include number of units required to form total lengths indicated.

Frame: [Gray-iron or galvanized steel for grates] [Not required].

Grates: Manufacturer's designation "[heavy] [medium] duty," with slots or perforations, and of width and thickness that fit recesses in channel sections.

Material: [Ductile iron] [Fiberglass] [Galvanized steel] [Gray iron] [Stainless steel] <Insert material>.

Locking Mechanism: [Manufacturer's standard device for securing grates to channel sections] [Not required].

Indicate locations and lengths of covers on Drawings.

Covers: Solid [ductile or gray iron] <Insert material>, of width and thickness that fit recesses in channel sections, and of lengths indicated.

Supports, Anchors, and Setting Devices: Manufacturer's standard, unless otherwise indicated.

Channel-Section Joining and Fastening Materials: As recommended by system manufacturer.

Narrow, Level-Invert, Polymer-Concrete Channel Drainage Systems <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 9878 option for 10-inch-wide polymer concrete trench drain.

Retain model 9895 option for 6-inch-wide polymer concrete trench drain.

Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; [9878] [9895]; <Insert product name or designation> or comparable product by one of the following:

ABT, Inc.

ACO USA.

Forté Composites, Inc.

Josam Company.

<Insert manufacturer's name>.

Description: Modular system of channel sections, grates, and appurtenances; designed so grates fit into channel recesses without rocking or rattling.

Indicate locations and lengths of covers on Drawings.

Channel Sections: Narrow, interlocking-joint, precast, polymer-concrete modular units with end caps.

Include rounded bottom, with level invert and with NPS 4 (DN 100) outlets in number and locations indicated.

Dimensions: [5-inch (127-mm)] <Insert dimension> inside width and [9-3/4 inches (248 mm)] <Insert dimension> deep. Include number of units required to form total lengths indicated.

Frame: [Gray-iron or galvanized steel for grates] [Not required].

Grates: Manufacturer's designation "[heavy] [medium] duty," with slots or perforations, and of width and thickness that fit recesses in channel sections.

Material: [Ductile iron] [Fiberglass] [Galvanized steel] [Gray iron] [Stainless steel] <Insert material>.

Locking Mechanism: [Manufacturer's standard device for securing grates to channel sections] [Not required].

Indicate locations and lengths of covers on Drawings.

Covers: Solid [ductile or gray iron] <Insert material>, of width and thickness that fit recesses in channel sections, and of lengths indicated.

Supports, Anchors, and Setting Devices: Manufacturer's standard, unless otherwise indicated.

Channel-Section Joining and Fastening Materials: As recommended by system manufacturer.

Indicate locations and lengths of covers on Drawings.

Wide, Level-Invert, Polymer-Concrete Channel Drainage Systems <Insert drawing designation if any>

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific 14-inch, polymer concrete trench drain product or a comparable product from manufacturers listed.

Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; model [9879]; <Insert product name or designation> or comparable product by one of the following:

ABT, Inc.

ACO USA.

Josam Company.

Polycast: Hubbell Power Systems, Inc.

<Insert manufacturer's name>.

Description: Modular system of channel sections, grates, and appurtenances; designed so grates fit into channel recesses without rocking or rattling.

Channel Sections: Wide, interlocking-joint, precast, polymer-concrete modular units with end caps.

Include flat or rounded bottom, with level invert and with outlets in number, sizes, and locations indicated.

Dimensions: [8-inch (203-mm)] <Insert dimension> inside width and [13-3/4 inches (350 mm)] <Insert dimension> deep. Include number of units required to form total lengths indicated.

Frame: [Gray-iron or galvanized steel for grates] [Not required].

Grates: Manufacturer's designation "[heavy] [medium] duty," with slots or perforations, and of width and thickness that fit recesses in channel sections.

Material: [Ductile iron] [Fiberglass] [Galvanized steel] [Gray iron] [Stainless steel] <Insert material>.

Locking Mechanism: [Manufacturer's standard device for securing grates to channel sections] [Not required].

Indicate locations and lengths of covers on Drawings.

Covers: Solid [ductile or gray iron] <Insert material>, of width and thickness that fit recesses in channel sections, and of lengths indicated.

Supports, Anchors, and Setting Devices: Manufacturer's standard, unless otherwise indicated.

Channel-Section Joining and Fastening Materials: As recommended by system manufacturer.

FRP Channel Drainage Systems <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 9812 option for 10-inch-wide FRP trench drains.

Retain model 9872 option for 12-inch-wide FRP trench drains.

          - Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; model [9812] [9872]; <Insert product name or designation> or comparable product by one of the following:

ACO USA.

Aquaduct, Inc.

Zurn Industries, LLC.

<Insert manufacturer's name>.

Description: Modular system of channel sections, grates, and appurtenances; designed so grates fit into channel recesses without rocking or rattling.

Channel Sections: Interlocking-joint, sloped-invert, FRP modular units, with end caps. Include flat, rounded, or inclined inside bottom, with outlets in number, sizes, and locations indicated.

Dimensions: [4 inches (102 mm)] [4 or 6 inches (102 or 152 mm)] [6 inches (152 mm)] [6 or 8 inches (152 or 203 mm)] [8 inches (203 mm)] wide. Include number of units required to form total lengths indicated.

Frame: [Galvanized steel] [Stainless steel] [Manufacturer's standard metal] <Insert material> for grates.

Grates: With slots or perforations and widths and thickness that fit recesses in channel sections.

Material: [Fiberglass] [Galvanized steel] [Gray iron] [Stainless steel] <Insert material>.

Locking Mechanism: [Manufacturer's standard device for securing grates to channel sections] [Not required].

Covers: Solid [ductile or gray iron] <Insert material>, of width and thickness that fit recesses in channel sections, and of lengths indicated.

Supports, Anchors, and Setting Devices: Manufacturer's standard, unless otherwise indicated.

Channel-Section Joining and Fastening Materials: As recommended by system manufacturer.

HDPE or PE Channel Drainage Systems <Insert drawing designation if any>:

Retain "Manufacturers" Subparagraph and list of manufacturers below to require products from manufacturers listed or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by one of the following:

Sioux Chief Manufacturing Company, Inc.

Tuf-Tite Corporation.

Zurn Industries, LLC.

<Insert manufacturer's name>.

Description: Modular system of channel sections, grates, and appurtenances; designed so grates fit into channel recesses without rocking or rattling.

Channel Sections: Interlocking-joint, HDPE or PE modular units, with end caps. Include flat, rounded, or inclined bottom, with level invert and with outlets in number, sizes, and locations indicated.

Dimensions: 4 inches (102 mm) wide. Include number of units required to form total lengths indicated.

Grates: With slots or perforations and widths and thickness that fit recesses in channel sections.

Material: [Fiberglass] [Galvanized steel] [Gray iron] [Stainless steel] <Insert material>.

Color: <Insert color or delete subparagraph>.

Supports, Anchors, and Setting Devices: Manufacturer's standard, unless otherwise indicated.

Channel-Section Joining and Fastening Materials: As recommended by system manufacturer.

PP Channel Drainage Systems <Insert drawing designation if any>:

Retain "Basis-of-Design Product" Subparagraph and list of manufacturers below to require a specific product or a comparable product from manufacturers listed.

Retain model 9930 option for 6-inch-wide polypropylene trench drains.

Retain model 9931 option for 6-inch-wide polypropylene trench drains, with steel frame for extra heavy applications.

          - Basis-of-Design Product: Subject to compliance with requirements, provide J.R. Smith Manufacturing; model [9930] [9931]; <Insert product name or designation> or comparable product by one of the following:

Infinity Plastics, Inc.

<Insert manufacturer's name>.

Description: Modular system of channel sections, grates, and appurtenances; designed so grates fit into channel recesses without rocking or rattling.

Channel Sections: Interlocking-joint, PP modular units, with end caps. Include flat, rounded, or inclined bottom, with level invert and with outlets in number, sizes, and locations indicated.

Dimensions: 4 inches (102 mm) wide. Include number of units required to form total lengths indicated.

Grates: With slots or perforations and widths and thickness that fit recesses in channel sections.

Material: [Fiberglass] [Galvanized steel] [Gray iron] [Stainless steel] <Insert material>.

Color: <Insert color or delete subparagraph>.

Supports, Anchors, and Setting Devices: Manufacturer's standard, unless otherwise indicated.

Channel-Section Joining and Fastening Materials: As recommended by system manufacturer.

PVC Channel Drainage Systems <Insert drawing designation if any>:

Retain "Manufacturers" Subparagraph and list of manufacturers below to require products from manufacturers listed or a comparable product from other manufacturers.

Manufacturers: Subject to compliance with requirements, provide products by one of the following:

MultiDrain Systems, Inc.

NDS Inc.

<Insert manufacturer's name>.

Description: Modular system of channel sections, grates, and appurtenances; designed so grates fit into channel recesses without rocking or rattling.

Channel Sections: Interlocking-joint, PVC modular units, with end caps. Include flat, rounded, or inclined bottom, with level invert and with outlets in number, sizes, and locations indicated.

Dimensions: 4 inches (102 mm) wide. Include number of units required to form total lengths indicated.

Grates: With slots or perforations and widths and thickness that fit recesses in channel sections.

Material: [Fiberglass] [Galvanized steel] [Gray iron] [Stainless steel] <Insert material>.

Color: <Insert color or delete subparagraph>.

Supports, Anchors, and Setting Devices: Manufacturer's standard, unless otherwise indicated.

Channel-Section Joining and Fastening Materials: As recommended by system manufacturer.

EXECUTION

INSTALLATION

In this article, retain only those sanitary piping specialties that are specified in Part 2. Additional instructions may be required for special applications. Indicate locations of specialties in plans, details, and schematics on Drawings.

Install floor drains at low points of surface areas to be drained. Set grates of drains flush with finished floor, unless otherwise indicated.

Coordinate first three subparagraphs below with Drawings.

Position floor drains for easy access and maintenance.

Set floor drains below elevation of surrounding finished floor to allow floor drainage.

Set with grates depressed in accordance with the following drainage area radii:

Radius, 30 Inches (750 mm) or Less: Equivalent to 1 percent slope, but not less than 1/4-inch (6.35-mm) total depression.

Radius, 30 to 60 Inches (750 to 1500 mm): Equivalent to 1 percent slope.

Radius, 60 Inches (1500 mm) or Larger: Equivalent to 1 percent slope, but not greater than 1-inch (25-mm) total depression.

Coordinate first subparagraph below with Drawings.

Install floor-drain flashing collar or flange, so no leakage occurs between drain and adjoining flooring.

Maintain integrity of waterproof membranes where penetrated.

Install individual traps for floor drains connected to sanitary building drain, unless otherwise indicated.

Install trench drains at low points of surface areas to be drained.

Set grates of drains flush with finished surface, unless otherwise indicated.

Retain first paragraph below if stainless steel channel drains complying with ASME A112.3.1 are required.

Comply with ASME A112.3.1 for installation of stainless steel channel drainage systems.

Install on support devices, so that top will be flush with adjacent surface.

Install FRP channel drainage system components on support devices, so that top will be flush with adjacent surface.

Install plastic channel drainage system components on support devices, so that top will be flush with adjacent surface.

Install open drain fittings with top of hub [1 inch (25 mm)] [2 inches (51 mm)] <Insert dimension> above floor.

CONNECTIONS

Coordinate piping installations and specialty arrangements with schematics on Drawings and with requirements specified in piping systems. If Drawings are explicit enough, these requirements may be reduced or omitted.

Comply with requirements in Section 221316 "Sanitary Waste and Vent Piping" for piping installation requirements. Drawings indicate general arrangement of piping, fittings, and specialties.

Comply with requirements in Section 221319 "Sanitary Waste Piping Specialties" for backwater valves, air admittance devices and miscellaneous sanitary drainage piping specialties.

Comply with requirements in Section 221323 "Sanitary Waste Interceptors" for grease interceptors, grease-removal devices, oil interceptors, sand interceptors, and solid interceptors.

Install piping adjacent to equipment to allow service and maintenance.

Ground equipment in accordance with Section 260526 "Grounding and Bonding for Electrical Systems."

Connect wiring in accordance with Section 260519 "Low-Voltage Electrical Power Conductors and Cables."

LABELING AND IDENTIFYING

Distinguish among multiple units, inform operator of operational requirements, indicate safety and emergency precautions, and warn of hazards and improper operations, in addition to identifying unit. Nameplates and signs are specified in Section 220553 "Identification for Plumbing Piping and Equipment."

PROTECTION

Protect drains during remainder of construction period to avoid clogging with dirt or debris and to prevent damage from traffic or construction work.

Place plugs in ends of uncompleted piping at end of each day or when work stops.

END OF SECTION 221319.13